## Slide 1
Lab 5 – Map Projection, Mosaics, Bundle Adjustments and other fun!
https://isis.astrogeology.usgs.gov

## Slide 2
Find Data Using Pilot
https://pilot.wr.usgs.gov/index.php
Demo of Pilot Search
Talk about Map Projection On the Web (POW)

## Slide 3: ISIS Photogrammetry can be complicated – we’ll keep it simple A more detailed USGS presentation is appended at the end of this file.

## Slide 4
Uncontrolled Mosaic Example - Preparation
Use the directory MDIS_example
Demo: using lists in ISIS programs
Create Level 1 products
Inspect with qmos & qview
qview lev1.lis
qmos lev1.lis
### Prepare Directories
ls EDR/*.IMG | cut -d"/" -f2 | cut -d"." -f1 >! names.lis
mkdir Lev0
mkdir Lev1
mkdir Lev2
### Create level 0 cubes and add spice data to them
mdis2isis from=EDR/\$1.IMG to=Lev0/\$1.lev0.cub -batch=names.lis
spiceinit from=Lev0/\$1.lev0.cub -batch=names.lis web=yes url=https://astrogeology.usgs.gov/apis/ale/v0.9.1/spiceserver/
### Calibrate images and add footprint info
mdiscal from=Lev0/\$1.lev0.cub to=Lev1/\$1.lev1.cub -batch=names.lis
camstats from=Lev1/\$1.lev1.cub attach=true linc=10 sinc=10 -batch=names.lis
footprintinit from=Lev1/\$1.lev1.cub linc=10 sinc=10 maxemission=89 maxincidence=89 increaseprecision=true -batch=names.lis
ls Lev1/*.cub >! lev1.lis

## Slide 5
A single map projection template is needed…
For later mosaicking, all projected images need to utilize the same resolution, projection, longitude domain, latitude type etc…
Demo maptemplate
Examine sinu.map
Project images and Mosaic with different blending strategies
Uncontrolled Mosaic Example – Map Projection
### Try a ‘quick’ map projection
cam2map from=Lev1/\$1.lev1.cub to=Lev2/\$1.lev2.cub map=sinu.map pixres=map -batchlist=names.lis
ls Lev2/*.cub >! lev2.lis
### Mosaic with different blending strategies
automos fromlist=lev2.lis mosaic=slapdash.cub matchbandbin=false priority=average
equalizer fromlist=lev2.lis process=both
ls Lev2/*equ.cub >! lev2.equ.lis
automos fromlist=lev2.equ.lis mosaic=equ_slapdash.cub matchbandbin=false priority=average
### USE QVIEW TO VIEW THE RESULT - note the seams and offsets
qview equ_slapdash.cub

## Slide 6
These MDIS data are very well-behaved
Uncontrolled mosaics work great

## Slide 7
Demo a repeat with CTX data – see LAB5_CTX_SCRATCH.txt
Uncontrolled Mosaic Example – 2nd example (if time allows)

## Slide 8
Based on a USGS tutorial using Messenger data
Use the MDIS_Controlled_example folder and steps in the LAB5_FULL_SCRATCH.txt file
Major Steps:
Find overlaps between images
Seed with Control points
Massage the Control Network
Use pointreg to refine control point positions
Use jigsaw to update the pointing kernels
Map Project and Mosaic the images.
Controlled Mosaic Example
Can be an iterative process with lots of human intervention

## Slide 9: Pre-processing – Cleanup the data
### Prepare Directories
ls EDR/*.IMG | cut -d"/" -f2 | cut -d"." -f1 >! names.lis
mkdir Lev0
mkdir Lev1
mkdir Lev2
### Create level 0 cubes and add spice data to them
mdis2isis from=EDR/\$1.IMG to=Lev0/\$1.lev0.cub -batch=names.lis
spiceinit from=Lev0/\$1.lev0.cub -batch=names.lis web=yes url=https://astrogeology.usgs.gov/apis/ale/v0.9.1/spiceserver/
### Calibrate images and add footprint info
mdiscal from=Lev0/\$1.lev0.cub to=Lev1/\$1.lev1.cub -batch=names.lis
camstats from=Lev1/\$1.lev1.cub attach=true linc=10 sinc=10 -batch=names.lis
footprintinit from=Lev1/\$1.lev1.cub linc=10 sinc=10 maxemission=89 maxincidence=89 increaseprecision=true -batch=names.lis
ls Lev1/*.cub >! lev1.lis
Import the PDS files into the USGS ISIS software (bundled with ASP)
Add the SPICE info on spacecraft pointing and position (note we use the USGS SPICE web service – the URL changed recently and may change again in future ISIS releases)
Calibrate the images

## Slide 10
Check progress with:
qmos lev1.lis
Try a quick uncontrolled map projection and mosaic
### Try a ‘quick’ map projection
cam2map from=Lev1/\$1.lev1.cub to=Lev2/\$1.lev2.cub map=sinu.map pixres=map -batchlist=names.lis
ls Lev2/*.cub >! lev2.lis
### Mosaic with different blending strategies
automos fromlist=lev2.lis mosaic=slapdash.cub matchbandbin=false priority=average
equalizer fromlist=lev2.lis process=both
ls Lev2/*equ.cub >! lev2.equ.lis
automos fromlist=lev2.equ.lis mosaic=equ_slapdash.cub matchbandbin=false priority=average
### USE QVIEW TO VIEW THE RESULT - note the seams and offsets
qview equ_slapdash.cub
Not so hot…. But we can improve the outcome with control points

## Slide 11
But equalization works well…. qview slapdash.cub equ_slapdash.cub

## Slide 12: Pre-processing – Bundle Adjust
findimageoverlaps
autoseed – creates points based on your image overlaps
seedgrid – only knows about the lat/lon/spacing
cnetadd – adds the image list you’re using
cnetedit – downselects to the points that cover the images
findimageoverlaps fromlist=lev1.lis overlaplist=overlaps.dat errors=ovl.err detailed=true
overlapstats fromlist=lev1.lis overlaplist=overlaps.dat
### Examine seed.def
autoseed fromlist=lev1.lis overlaplist=overlaps.dat deffile=seed.def onet=auto.net errors=auto.err pointid="mess_??" networkid=MESS description="Ptys551"
Two possible strategies
We use this one

## Slide 13
Check progress with:
qmos lev1.lis
### USE QMOS TO VIEW THE FOOTPRINTS + CONTROL NET
qmos lev1.lis
### Use qnet for additional info
qnet
### File->Open Control Net and Cube List->lev1.lis and then auto.net
### Triage the control network by eliminating useless points
### Examine validmsr.def
cnetref fromlist=lev1.lis cnet=auto.net onet=auto_ref.net log=auto_ref.log deffile=validmsr.def criteria=resolution type=mean
cnetedit cnet=auto_ref.net onet=auto_ref_edit.net

## Slide 14: Pre-processing – Check the Control network with Qnet
Start qnet
File -> Open control network and cube list
Select lev1.lis and auto.net
Select the first control point listed in the ‘Control Network Navigator’ window. Click the ‘View Cube(s)’ button.
Click any of the points on the image display to open the Qnet tool.
(check the Geom button in the lower right when comparing images)
In the Qnet tool you can delete or modify points, blink-compare them etc…
Some networks are huge... The global MDIS mosaic control net has 12.5 million points

## Slide 15: Pre-processing – pointreg
### Try all points with a tight search chip
pointreg fromlist=lev1.lis cnet=auto_ref_edit.net onet=auto_ref_edit_reg.net deffile=pointreg_P31x31_S101x101.def flatfile=auto_ref_edit_reg.txt points=all measures=all
### Try the failed points again with a wide search chip
pointreg fromlist=lev1.lis cnet=auto_ref_edit_reg.net onet=auto_ref_edit_reg2.net deffile=pointreg_P135x135_S200x200_gradient.def flatfile=auto_ref_edit_reg2.txt points=all measures=candidates
### Remove points that are total failures
cnetedit cnet=auto_ref_edit_reg2.net onet=auto_ref_edit_reg2_edit.net
### Quality checks on the control network
cnetcheck fromlist=lev1.lis cnet=auto_ref_edit_reg2_edit.net prefix=Chk_ tolerance=0.0
cnetstats fromlist=lev1.lis cnet=auto_ref_edit_reg2_edit.net create_image_stats=yes image_stats_file=ImgStats_auto_ref_edit_reg2_edit.csv create_point_stats=yes point_stats_file=PtStats_auto_ref_edit_reg2_edit.csv
Object = AutoRegistration
Group = Algorithm
Name = MaximumCorrelation
Tolerance = 0.8
End_Group
Group = PatternChip
Samples = 31
Lines = 31
End_Group
Group = SearchChip
Samples = 101
Lines = 101
End_Group
Group = SurfaceModel
DistanceTolerance = 1.5
WindowSize = 7
End_Group
End_Object
End
Another def file (pointreg_P31x31_S101x101.def) describes how to do the pattern matching. e.g.
How large is the pattern?
How large is the search area?
How good a match is ok?

## Slide 16: Jigsaw !!
jigsaw fromlist=lev1.lis cnet=auto_ref_edit_reg2_edit.net onet=JigOut.net update=no radius=no errorpropagation=no outlier_rejection=no sigma0=1.0e-10 maxits=10 camsolve=angles twist=yes spsolve=no camera_angles_sigma=0.025
### Inspect for problems here. Remove bad (high residuals; see below) points in qnet if needed.
### Setup new directory for adjusted level 1 cubes and run jigsaw for realz
cp -R Lev1 Updated_Lev1
ls Updated_Lev1/*cub >! lev1_updated.lis
jigsaw fromlist=lev1_updated.lis cnet=auto_ref_edit_reg2_edit.net onet=JigOut.net update=yes radius=no errorpropagation=no outlier_rejection=no sigma0=1.0e-10 maxits=10 camsolve=angles twist=yes spsolve=no camera_angles_sigma=0.025
We first run jigsaw as a dry-run i.e. no change to the image cubes
We then check the residuals for all the points in the jigsaw solution to see if there are any problematic ones…
Open the file bundleout_points.csv and sort by the Residual RMS (column E)

## Slide 17: Map project the new cubes!
Jigsaw has altered the SPICE data so the pointing and the position of the spacecraft has been refined and control points are solved for in 3D space
### Make a new directory for updated level 2 cubes and map-project
mkdir Updated_Lev2
cam2map from=Updated_Lev1/\$1.lev1.cub to=Updated_Lev2/\$1.lev2.cub map=sinu.map pixres=map -batchlist=names.lis
ls Updated_Lev2/*.cub >! lev2_updated.lis
### Mosaic with different blending strategies
automos fromlist=lev2_updated.lis mosaic=updated_slapdash.cub matchbandbin=false priority=average
equalizer fromlist=lev2_updated.lis process=both
ls Updated_Lev2/*equ.cub >! lev2_updated.equ.lis
automos fromlist=lev2_updated.equ.lis mosaic=equ_updated_slapdash.cub matchbandbin=false priority=average
### Don’t bother with Blend in this example, but the code is below for reference
blend fromlist=lev2_updated.lis stop=200
ls Updated_Lev2/*blend.cub >! lev2_updated.blend.lis
automos fromlist=lev2_updated.blend.lis mosaic=blend_updated_slapdash.cub matchbandbin=false priority=average

## Slide 18
Worth it? Totally. qview equ*slapdash.cub

## Slide 19: ISIS Photogrammetric Control Processes
Tammy L. Becker
Kris J. Becker
March 4, 2021

## Slide 20
ISIS3 Controlled Map Product Development
20
Radiometric
Calibration
(Level 1
or
Ingested CDR)
Shape Model:
-DEM
-Socet/Set DEM Product
Target Body:
-Ellipsoid/Sphere
Map
Projection
(Level2)
cam2map
SPICEINIT
(Level 0)
Updated Image
Labels
Uncontrolled Mosaic
Build Control Point Network
Jigsaw: Bundle Adjustment
Solution, Accuracy,
Error and Analysis
Images
Images
Ingested
RAW-
EDR
Images
Controlled Mosaic
Expanded On Next Slide
DEM/Radius
-LOLA
-MOLA
-Gaskell
Sphere
Controlled Mosaic
Mosaic
automos
C-Smithed Kernels
-new adjusted SPICE

## Slide 21
SeedGrid
Establish Lat/Lon
Increment
CnetAdd
Add image
measures
footprintinit
findimgoverlaps
AutoSeed
Images
Spiceinit
Apriori
NAIF/
SPICE
camstats
attach=True
QMOS
Display
Footprints
Pointreg
Measurement
Coregistration
Digital
Elevation
Model
Target
Body
Ellipsoid/
Sphere
Jigsaw
SocetSet
Points +Msmts
(with Ground)
Mat2Cnet
Isis2toIsis3
NASA/AMES
Network
“Add/Edit “
Constraint
Sigmas into
Network
“Ground”
Sources
Other
“NetWork”
Sources in PVL format
Images
Updated
Images
Labels
QNET
Autoregtemplate
Create co-reg
PVL file or QNET
PVL file editor
Digital Image
BaseMap
Jigsaw Reports
Output
Network
CnetHist
CnetWinnow
Clean
Network of
Blunders
overlapstats
Statistics/data of
footprint
information
Shape
Model
(DEM)
CKwriter
Generate
C-smithed
Camera kernel
SPKwriter
Generate
C-smithed
Spacecraft-kernel
QMOS
Display
Network
Points
CnetEditor
Interactive Sort
Filter, Modify
Network
CnetSplit
Separate Single
Network
into multiple
CnetMerge
Merge Separate
Networks into a
Single Network
CnetRef
Establish
Reference Images
for each Point
CnetExtract
Create a
Sub-Network
from a Main
CnetEdit
Modify
Network
CnetNewRadii
Update Radius
values
in Network
CnetStats
Stats on network
Images, Points,
Msrs
CnetBin2PVL
Convert Binary
Network to PVL
format
CnetDiff
Difference
Network Files
Images
Data Prep; know your data
Initial Control Net
Path 1 – by image overlap
Initial Control Net
Path 2 – by grid spacing
CnetCheck
Network Quality
Control
CnetTable
Campt information
Based on network
Points and Msrs
ISIS3 Photogrammetry

## Slide 22: Initiating a control network involves a choice of two paths
FIRST: Know your data!
  camstats
    camera statistics for a single image or all images
    attach=true for qmos
    Increase linc & sinc to 10 to 100 the default = 1 (slow)
  footprintinit - create polygons from images for qmos
  qmos - overlaps and basic camera statistics
  qview - image quality, pointing quality, overlap amounts
  mosrange - latitude/longitude, resolution range for all images in map file format
  caminfo - good for a large amount of images. camera statistics, geometry information, DN statistics,
    label and polygon information (in WKT format) for a single image or all images
Familiarity with your data regarding…
1) how the images overlap
2) range of resolution
3) viewing & illumination conditions
will help determine the best path for establishing your network…
by image overlaps (path1) and/or
by a gridded control point distribution (path2)
*There is no right or wrong method, there could be a combination of the paths

## Slide 23: Initiating a control network involves a choice of two paths
CTX Footprints
Candidate for either path
Messenger Flyby Footprints:
Candidate for autoseed path
LROC NAC Polar Footprints
Candidate for seedgrid path

## Slide 24
findimageoverlaps
autoseed – based on your image overlaps
seedgrid – doesn’t know a thing about your images, only the lat/lon/spacing
The initial goal is to have a sufficient distribution of control point image measures across and through the image overlaps and across your images where possible
qmos-footprint display
qmos-footprint display
Starting a Control Network from scratch with Image Overlaps v.s. Gridded Points

## Slide 25
findimageoverlaps
autoseed
*Has the potential to see every single overlap polygon
seedgrid map=spolar_projection.map
cnetadd retrieval=point extract=modified
*Every image in the stack needs a good distribution

## Slide 26
seedgrid
with moderate X/Y Spacing
seedgrid
with less dense X/Y Spacing
X/Y Spacing starting point
  Determined by resolution(s), overlap area(s) and desired number of points in overlaps
Try to strike a balance with the number of points seeded
  Too many points
    Increases program runtime
    Increases potential number of registration false positives
  Too few points
    May result in poorly connected the data
    May result in more manual point picking than desired

## Slide 27
findimageoverlaps
autoseed – based on your image overlaps
Spacing a little too dense maybe?
Minimum Area Too Thick
Just right
Spacing too sparse for small overlaps
::::::::::::::
grid.def
::::::::::::::
Group = PolygonSeederAlgorithm
Name = Grid
MinimumThickness = 0.1
MinimumArea = 56000
XSpacing = 15000 #40000
YSpacing = 15000 #40000
End_Group
::::::::::::::
grid.def
::::::::::::::
Group = PolygonSeederAlgorithm
Name = Grid
MinimumThickness = 0.3
MinimumArea = 56000
XSpacing = 25000
YSpacing = 25000
PixelsFromEdge = 35
End_Group

## Slide 28
Avoid control point image measures in the shadows with a MinDN and or a maximum incidence angle (MaxIncidence) for the terminator region
Avoiding undesirable data (shadows, limb, terminator, edges, no data, etc.)
  Use valid measure deffile and desired settings
    $ISIS3DATA/base/templates/cnet_validmeasure/validmeasure.def
    Can be applied anytime in an application that offers a ‘deffile’ parameter
      cnetedit deffile=valid.def
      findimageoverlaps/autoseed: autoseed deffile=valid.def
      seedgrid/cnetadd: cnetadd deffile=valid.def
Group = ValidMeasure
MinDN = 0.001
MaxDN = double
MinEmission = double (limb/oblique criteria)
MaxEmission = double
MinIncidence = double (terminator/shadow)
MaxIncidence = 75 (degrees)
MinResolution = double
MaxResolution = double
PixelsFromEdge = integer OR MetersFromEdge = double
EndGroup

## Slide 29
Avoid control point image measures in the shadows with a MinDN and along the edges of the image with PixelsFromEdge
Green “+” = Valid Measures; Yellow “+” = Invalid Measures (Ignore = True)
Avoiding undesirable data (shadows, limb, terminator, edges, no data, etc.)
  Use valid measure deffile and desired settings $ISIS3DATA/base/templates/cnet_validmeasure/validmeasure.def
    Can be applied anytime in an application that offers a ‘deffile’ parameter
      cnetedit deffile=valid.def
      findimageoverlaps/autoseed: autoseed deffile=valid.def
      seedgrid/cnetadd: cnetadd deffile=valid.def
Group = ValidMeasure
MinDN = 1.5
MaxDN = double
MinEmission = double (limb/oblique criteria)
MaxEmission = double
MinIncidence = double (terminator/shadow)
MaxIncidence = double
MinResolution = double
MaxResolution = double
PixelsFromEdge = 20
EndGroup

## Slide 30
footprintinit
findimgoverlaps
autoseed
Images
Spiceinit
Apriori
NAIF/
SPICE
QNET
footprintinit: Create footprint polygons for each image
  Provides footprint polygons for qmos
    Required for findimageoverlaps & autoseed
    Set maxemission and maxincidence for limb and terminator data
    Consider a smaller linc and sinc for limb, polar or irregularly shaped data
    Set increaseprecision=true for automatic adjustment with linc and sinc to smaller values if current values result in invalid polygons
findimageoverlaps: Create a binary file of overlapping polygons
overlapstats: Compute overlap polygon statistics
  Input file is the findimageoverlaps output
  View output of overlapstats for help with setting initial parameter values in the autoseed ‘deffile’
autoseed: Create a distribution of control points across the areas of overlap
  autoseed Workshop!!
    http://isis.astrogeology.usgs.gov/IsisWorkshop/index.php/Autoseed
  autoseed deffile templates
    cp $ISIS3DATA/base/templates/autoseed/grid.def mygrid.def
    Set optional ‘valid measure’ parameters within the autoseed deffiile (mygrid.def)
      $ISIS3DATA/base/templates/autoseed/gridExtraKeywords.pvl
      Examples-avoid the edges of an image, high emission angles, shadows
Commands:
> footprintinit from= linc= sinc= maxema= maxinc= (use –batchlist)
> findimageoverlaps fromlist= overlaplist=overlap.dat
> overlapstats fromlist= overlaplist=overlap.dat to=overlap.csv
  > autoseed fromlist= overlaplist=overlap.dat deffile=mygrid.def onet=autoseed.net pointid=“prefix_???”
qnet - Load the image list and autoseed.net file; view some number of cubes to evaluate the control point distribution in Level1 (raw camera space)
qmos - Overlay the output autoseed.net file on top of the image footprints to evaluate control point distribution
Images
camstats
attach=true
qmos
Path1: Starting a Control Network from scratch using Image Overlaps
overlapstats
Data Prep & know your data
Optimize a point distribution in overlaps with autoseed
Visualize the results in both qmos and qnet
Images
calibrated/
clean

## Slide 31
footprintinit
cnetadd
Images
Spiceinit
Apriori
NAIF/
SPICE
QNET
footprintinit: Create footprint polygons for each image (for qmos)
seedgrid: Create a distribution of control points across the areas of overlap
  Establish grid by XY meters or latitude/longitude increment (spacing parameter)
  Note how many control points are created!!
  See Autoseed Worshop for tips on setting spacing
    http://isis.astrogeology.usgs.gov/IsisWorkshop/index.php/Autoseed
Create a ‘valid measure’ parameter file
  Possible parameters for valid criteria with an image measure are listed in
    $ISIS3DATA/base/templates/cnet_validmeasure/validmeasure.def.example
  Create your own parameter file to edit
    cp $ISIS3DATA/base/templates/cnet_validmeasure/validmeasure.def.example validmsr.def
  Edit the validmsr.def to establish optional criteria
    Examples-avoid the edges of an image, high emission angles, shadows
cnetadd: Add the image measures
  Based on who overlaps the control point lat/lon’s created in seedgrid
  Supply the valid measure criteria parameter file (deffile)
    Any measure added to a control point considered invalid will have Ignore=True
cnetedit: Delete the ‘Ignored’ points from the network
  NOTE: future application cnetref might fail if this step is elminated
    Potential problem with control points that contain no image measures (no one overlaps that point)
Commands:
  > footprintinit from= linc= sinc= maxema= maxinc= (use –batchlist)
  > seedgrid target= minlat= maxlat= minlon= maxlon= spacing= desc= pointid=“prefix_???”
  > cnetadd fromlist= deffile=validmsr.def retrieval=point onet=cnetadd.net polygon=true
  extract=modified
  >cnetedit cnet=cnetadd.net onet=cnetadd-edt.net
>qnet - Load the image list and cnetadd-edt.net file; view a number of cubes to evaluate the control point distribution in Level1 (raw camera space)
>qmos - Overlay the output cnetadd-edt.net file on top of the image footprints to evaluate control point distribution
Images
Images
calibrated/
clean
camstats
attach=true
qmos
Path2: Starting a Control Network from Scratch Using Gridded Points
seedgrid
cnetedit
Visualize the results in both qmos (for footprint overlap view) and qnet (for Level1 view)
Data Prep & know your data

## Slide 32
Images
Spiceinit
Apriori
NAIF/
SPICE
QNET
pointreg
Measurement
Coregistration
cnetref: Establish the reference images for each control point (Optional-Use with Caution)!
  The measure (image) within a control point with Reference=True becomes the “pattern” chip in pointreg for the remaining measures
  The Reference measure is implicitly defaulted to the 1st measure encountered within a control point
    unless it is overridden interactively in qnet or cnetref
  cnetref will assign the image measure with Reference=True by a selection of criteria
    Criteria=emission (avoid the limb; the image measure with the lowest ema = reference)
    Criteria=incidence (avoid the terminator; the measure with the lowest inc=reference)
    Criteria = resolution (multiple criteria choices available to select the reference)
  Can use the same valid measure parameter file that is passed to cnetadd or …create/edit
    cp $ISIS3DATA/base/templates/cnetref/no_operator.def.example validmsr.def
  Criteria=interest ( “nudge” the control point locations to new coordinates in areas of interest)
    cp $ISIS3DATA/base/templates/cnetref/standard_deviation_operator.def.example std.def
pointreg: Pattern matching amongst the measures within each control point
  Subpixel registration matches the measures to the reference image
  Autoreg deffile template (create your own and edit)
    cp $ISIS3DATA/base/templates/autoreg/coreg.maxcor.p2020.s5050.def reg.def
  Pattern Match Workshop and Document
    http://isis.astrogeology.usgs.gov/documents/PatternMatch/PatternMatch.html
    http://isis.astrogeology.usgs.gov/IsisWorkshop/index.php/Automatic_Registration
    cnetedit: Delete the ‘Ignored’ measures and points
cnetcheck: Used to double check the quality of the network right before jigsaw
qnet: Used through the entire process for visual and manual adjustments
jigsaw: Least squares bundle adjustment-default is to solve for camera angles & twist
Commands:
  > cnetref fromlist= cnet= onet=cnetref.net deffile= criteria= type=
> pointreg fromlist= cnet=cnetref.net onet=pointreg.net deffile=reg.def points=all measures=all
>cnetedit cnet=pointreg.net onet=pointreg-edt.net
>cnetcheck fromlist= cnet=pointreg-edt.net prefix=pointreg-edt-CHK
> jigsaw fromlist= cnet=pointreg-edt.net onet=jig.net file-prefix=jig
Images
Images
calibrated/
clean
cnetref
Change Pt/msmt
Location and/or
establish reference
image
Cnet Utilities
cnetstats
cnetedit
cneteditor
cnetsplit
cnetmerge
cnetcheck
Network
Quality Control
Jigsaw
autoseed
seedgrid
cnetadd
cnetedit
Processing the Control Network
The next goal is to maximize the success and accuracy results of the sub-pixel registration amongst the image measures within each tie-point.
Processing the Control Network

## Slide 33
Use qnet to
  Define the autoreg parameter file (deffile)
  View registration ‘chips’ to iterate and optimize the parameters for automated success
  Refer to: http://isis.astrogeology.usgs.gov/IsisWorkshop/uploads/8/80/Qnet_demo.pdf
Pattern Chip
  The more ‘bland’ the data is, the larger the Pattern Chip box should be
Search Chip
  Should always be larger than Pattern chip
  The size needs to account for feature offset (misregistration)
    SearchChipSize = PatternChipSize + (OffsetPixelEstimate * 2)
  It should be unnecessarily large for the Pattern Chip to avoid a ‘false positive’ match
Pattern Matching the Image Measures

## Slide 34
Dimensions
  The overall shape of Search and Pattern chips should mimic your image data and how it overlaps where possible
  Long and skinny images and overlaps, then try long and skinny Pattern and Search chip size dimensions
Fit Chip
  Will match the dimension of the Search Chip
  Filled with the resulting Goodness of Fit values at every position that the Pattern Chip has been walked across the Search Chip computing a fit correlation value
  The Fit chip is only good to a maximum of ONE pixel accuracy
Strategize with complex datasets
  More than one registration definition file may be necessary to register all measures and points
    1st time: pointreg cnet=in.net onet=out-1.net deffile=reg-1.def points=all measures=all
    2nd time: pointreg cnet=out-1.net onet=out-2.net deffile=reg-2.def points=all measures=candidates
Pattern Matching the Image Measures

## Slide 35
Pattern Chip
25 samples x 25 lines
Search Chip
90 samples x 90 lines
Fit Chip
90 samples x 90 lines
  The Fit Chip is filled with the resulting
  Goodness of Fit (correlation value) value at every position that the Pattern Chip has been walked across the Search Chip
  The Pattern Chip is a sub-area extracted from the Reference image measure within a control point. The center of the chip is the coordinate sample and line
NULLs
NULLs
NULLs
NULLs
Sample 13
(25/2)
Pattern Chip
25 samples
x 25 lines
Line 13
(25/2)

## Slide 36
Pattern Chip
25 samples x 25 lines
Search Chip
90 samples x 90 lines
Fit Chip
90 samples x 90 lines
  The Fit Chip is filled with the resulting
  Goodness of Fit (correlation value) value at every position that the Pattern Chip has been walked across the Search Chip
  The sample, line coordinate of the highest value within the Fit Chip is used to compute the Adjusted Registered sample, line coordinate of the image measure.

## Slide 37
Fit Chip – 3D
90 samples x 90 lines
If SubPixelAccuracy = True (default), the Fit Chip is then passed onto a centroid surface modeling algorithm in order to refine the whole pixel registered sample, line coordinate to a sub-pixel accuracy
For more details refer to:
http://isis.astrogeology.usgs.gov/documents/PatternMatch/PatternMatch.html#SubPixelAccuracy

## Slide 38
Good distribution
Convex Hull = ~0.99
Bad distribution
Convex Hull < 0.5
Bad distribution
Convex Hull < 0.5
Control Point Distribution Across an Image
Before running jigsaw, the completeness and “health” of the input control network should be double checked
  -cnetcheck creates output files indicating network issues
  -The reported issues need to be addressed before running jigsaw
  -Most common issues
    Avoid single measures in a point (only one image in a control point)
      Optimum is more than 3 images/point at varying viewing angles to support convergence
    Avoid more than 1 “island”, if all images are tied together then a single island is reported
    Make sure each image contains greater than 3 or 5 control points
      Low coverage report (convex hull) indicates the distribution of the points across the image
Quality Control of a Network
The point measurement distribution across the area of the image is critical for both frame cameras and line scan cameras. Think of the measurements as anchor ties.
In addition, the distribution of the points in the context across the overlapping areas of the images is also important and should be thought of as anchor ties (tacks) through the ‘stack’ of images

## Slide 39
Example of control network “Islands”
Qmos:
Image footprints with a single control network overlaid
-disconnected islands
Island 1
Island 2
Island 4
Island 3
The blue “+” marks above are the control points overlaid on top of the image footprints by latitude and longitude position.
This is a single control net file and simply demonstrates what are considered islands where the images do not overlap.
Also, even though the images in Island1 overlap slightly with the images in Island2, qmos has indicated that these images do not share a control point

## Slide 40
Control Network Terminology (very, very brief for now)
Control Point Type
Free (no constraints) – also referred to as “tie-points”
Constrained (weighted to a ‘ground’) - also referred to as “ground-points”
Fixed (highest constraint possible to ‘ground’) - also referred to as “ground-points”
Apriori Latitude, Longitude, Radius
The location of the control point; a priori based on original SPICE
Computed by the first measure in the control point, or an average, or set when measured to a Ground reference (type=constrained or fixed)
Apriori Latitude, Longitude, Radius Sigmas
Parameters for weighing/constraining the location of the control point with type Contrained of or Fixed (set in qnet or cneteditor)
Adjusted Latitude, Longitude, Radius
The converged location of the control point after jigsaw
Ignore = True/False
If True, the control point and all measures are ignored by pointreg (optional) and jigsaw; cnetedit will remove these measures by default
Measurement The sample and line pixel coordinate of an image
Serial Number A unique identifier for every image constructed “on-the-fly” in the cnet applications using the instrument group keyword values. Internal to the control network; most applications will include the associated filename. To view a Serial Number run ‘getsn from=image.cub’
Sample, Line The image pixel coordinate
Measurement Type
Candidate: least accurate pixel measurement-usually based on apriori SPICE
Manual: measured manually in qnet
RegisteredSubPixel: output coordinate resulting from pointreg, or qnet-”Register” feature
Ignore = True/False (Measure)
If True, the measurement will be ignored by pointreg (optional) and jigsaw; cnetedit will remove these measures by default
Reference=True (Measure)
The image that is used as the ‘Pattern’ chip for the pattern matching of all remaining measures (image coordinates) within a control point
The 1st measure listed within a control point is implicitly set as Reference=true by most applications
*This can be overridden by the ‘cnetref’ application or interactively by the user within qnet (always the left hand image in the control point editor)
Will often remain measurement-type=candidate after pointreg
Goodness of Fit (Measure)
The pattern match correlation result for co-registration of measures to the reference
Sample/Line Residual (Measure)
Jigsaw residuals in pixels

## Slide 41
Contol Point Id 100
Type=Free, Constrained, Fixed
Apriori Latitude=
Apriori Longitude=
Apriori Radius=
Ignore=False/True
Measurement 1
Serial Number=AA
MeasureType=Candidate, Sub-Pixel, Manual
Reference=True
Sample=
Line=
Ignore=False/True
Control Point Id 200
Type=Free, Constrained, Fixed
Apriori Latitude=
Apriori Longitude=
Apriori Radius=
Ignore=False/True
Measurment 1
Serial Number=AA
MeasureType=Candidate, Sub-Pixel,Manual
Reference=False
Sample=
Line=
Ignore=False/True
Measurement 2
Serial Number=BB
MeasureType=Candidate,Sub-Pixel,Manual
Reference=True
Sample=
Line=
Ignore=False/True
Measurement 3
Serial Number=CC
MeasureType=Candidate,Sub-Pixel,Manual
Reference=False
Sample=
Line=
Ignore=False/True
Measurement 2
Serial Number=DD
MeasureType=Candidaet,Sub-Pixel,Manual
Reference=False
Sample=
Line=
Ignore=False/True
Control Point 100-Measure 1
Serial Number: AA
Control Point 100-Measure 3
Serial Number: CC
Control Point 100-Measure 2
Serial Number: DD
Control Point 200-Measure 1
Serial Number: AA
Control Point 200-Measure 2
Serial Number: BB
Image-XA.cub
Image-XD.cub
Image-XC.cub
Image-XB.cub
Control Network Schema
(Abbreviated Version)
Control Point Type
Free (no constraints) – also referred to as “tie-points” or “match-points”
Constrained (weighted to a ‘ground’) - also referred to as “ground-points”
Fixed (highest constraint possible to ‘ground’) - also referred to as “ground-points”

## Slide 42
Control (Ground) Points
Type=Constrained or Fixed
Control Point or Ground Point
  Represents a known location on the ground (latitude/longitude/radius)
  Sigma values or weights are assigned to each Control Point (indication of how accurate)
  Example known ‘Ground’ sources
    For radius/topography values at a location
      LOLA for Moon, MOLA for Mars, Gaskell DEM for Vesta
    For ‘horizontal’ latitude and longitude location values
      DEMs
      Basemaps
Distribution
  Control points need to be distributed across the ground coverage extents of the images
  Control points need to distributed across/within the overlaps of the images
  Refer to: http://isis.astrogeology.usgs.gov/IsisWorkshop/uploads/8/80/Qnet_demo.pdf

## Slide 43
Areas where additional
control points should be
collected
Control (Ground) Points
Type=Constrained or Fixed
Vesta – Gaskell DEM
Equirectangular
Shaded version
Pink marks indicate “ground” control point locations
  This example is somewhat sparse
Vesta – DAWN Image Overlaps
Equirectangular
Shaded version
Green marks indicate “ground” control points